## Slide 1: Autonomous Drone Engineer B4 – Software Architecture
Paul.Guermonprez@intel.com Autonomous Drone Solutions Architect

## Slide 2: Basic Drone Control

## Slide 3: Compute Board / Flight Controller
The Intel Aero RTF Drone has two parts:
A Flight Controller (FC), taking care of the stabilization, compass, GPS and other simple sensors: Intel Aero Flight Controller
A Compute Board running linux, taking care of the high level mission and complex sensors like Intel RealSense: Intel Aero Compute Board
The two components are connected over a serial port. The protocol used is MAVLINK, an industry standard.
Most drone software developers only need to develop software for the Compute Board running linux.
To pilot the drone, you send MAVLINK messages.

## Slide 4: Serial Port or Server Socket?
The default Linux build shipped with Intel Aero comes with a proxy software exposing the serial port as a network socket (port 5760) and sending MAVLINK messages over the network.
It is interesting for several reasons:
The MAVLINK messages can be sent to the calibration computer over the network: You don’t need a cable to calibrate your drone
Accessing a network port is easier than a serial port
Several software stacks can share the flight controller data and access
Conclusion: instead of sending MAVLINK messages over a serial port, we’ll send MAVLINK messages to the 5760 network port.

## Slide 5: Serial Port or Server Socket?
Linux running on Intel Aero Compute Board
PX4 or Ardupilot running on Intel Aero Flight Controller
Serial Port
QGroundControl running on the calibration computer
Low Level (MAVLINK) Network Sockets
MAVLINK Proxy
AD sw running on Yocto
Local Port 5760
Server backend
High Level (WebSocket, REST) Network Socket

## Slide 6: Serial Port or Server Socket?
Yocto Linux running on Intel Aero Compute Board
PX4 or Ardupilot running on Intel Aero Flight Controller
Serial Port
QGroundControl running on the calibration computer
Low Level (MAVLINK) Network Sockets
MAVLINK Proxy
Dockerized AD sw on Ubuntu
AD sw running on Yocto
Local Port 5760
Local Port 5760
Remote Control Software running on a ground computer
Server backend
High Level (WebSocket, REST) Network Socket

## Slide 7: MAVLINK Abstraction?
MAVLINK is an industry standard, APIs are available in various languages like C/C++ and Python. Drone developers should know the basics of MAVLINK. But it’s low level and not very friendly.
Several frameworks propose higher level abstractions and interfaces:
DroneCore, part of the DroneCode initiative. http://dronecore.io Designed for PX4.
MAVProxy, in Python http://ardupilot.github.io/MAVProxy/ Mostly works with Ardupilot Flight Controller Stack.
Module for ROS, the Robotic Operating System. More on ROS in the next slides. http://wiki.ros.org/mavlink
Dronekit, originally developed by 3D Robotics. Not very active lately, but still interesting. http://dronekit.io
Several startups developed friendly proprietary stacks on top of MAVLINK. You may encounter their stack if you buy one of their drones. Examples: DroneSmith, Drotek, OttoFly, Flylab … https://github.com/intel-aero/meta-intel-aero/wiki/80-Intel-Aero-Ecosystem

## Slide 8: Summary
Propositions:
Use QGroundControl to calibrate your drone and monitor the flight during development. It will use MAVLINK messages over the network. It is a convenient debug and development mode.
Learn the basics of MAVLINK.
Use MAVLINK abstractions to make the development of your autonomous drone logic simpler.
Avoid using the serial port directly, use port 5760.

## Slide 9: Autonomous Drone Development

## Slide 10: Sensors and Network
With MAVLINK over the port 5760, we can now write a software running on the Compute Board that will control the drone flight controller. Why do we want to do that?
Go beyond the simple GPS path: define/adapt the mission on the fly
Interact with the network (Wifi or LTE): receive instructions, traffic information, give feedback, upload data …
Interact with smart sensors like Intel RealSense, make decisions locally and quickly: collision avoidance, SLAM, follow target …

## Slide 11: How to use Intel RealSense from the RTF?
RealSense is not just a pair of cameras. It is a smart 3D sensor returning the fully computed 3D depth matrix to the Compute Board.
You can access this depth matrix directly with libRealSense: https://github.com/IntelRealSense/librealsense
If you want to use RealSense to avoid collisions, you can test this library and code your own library adapted to your specific needs: https://github.com/01org/collision-avoidance-library
To perform SLAM, you can use this library (but it will require a different RealSense camera: model ZR300): https://software.intel.com/sites/products/realsense/slam/developer_guide.html

## Slide 12: Computer Vision
The video devices included in the RTF Drone are accessible as standard V4L2 video devices (/dev/video*). You can access them by using the V4L2 library from the language of your choice or from the command line with gstreamer. Video devices are also exposed as RTSP streams. Typical usages:
Video recording and streaming: gstreamer, RTSP
Simple image analysis: OpenCV
Vision based 3D positioning and virtual servoing: VISP, ARToolkit
Reading QR Codes: zbar
Your custom code, using the library of your choice …

## Slide 13: ROS – Robotic Operating System
It may be tricky to integrate several libraries like MAVLINK, VISP, RealSense together. ROS is a way to unify the interfaces and simplify the integration of components coming from various sources.
ROS is not an operating system, it’s a stack running on top of the Linux OS (Yocto or Docker-Ubuntu in our case).
ROS has modules such as:
MavROS for MAVLINK http://wiki.ros.org/mavros
VISP http://wiki.ros.org/visp
OpenCV http://wiki.ros.org/vision_opencv
RealSense http://wiki.ros.org/RealSense

## Slide 14: Summary
Once you understood the basics of drone control over MAVLINK, you have a vast choice of libraries at your disposal.
Some come from Intel, like the RealSense related libraries.
Other from the Open Source ecosystem, like Computer Vision libraries VISP, ARtoolkit, OpenCV.
And you can always code your own, using the language of your choice.
Intel Aero is an open platform, the limit is your imagination.

## Slide 15: Thanks
Paul.Guermonprez@intel.com
https://intel-aero.github.io
Released under Creative Commons-BY creativecommons.org/licenses/by/2.0/